## Slide 1: Swift workflow example - auxetic
Workflow to automatically optimize materials design problem
Considers a network of particles connected by bonds which can be selected and cut to optimize the material response under stress
Since any combination of bonds may be cut, there is an extremely large search space (limited only by physical constraints)
Each Auxetic task is a call to a C++ function that measures the impact of a given cut on the system
  For a 300 particle test system, this takes ~1.8s on Midway (UofC cluster)
The C++ functionality is exposed via Python interfaces (Boost.Python)
A Swift workflow orchestrates the search and distributes work across Midway
Collaboration with Daniel Reid (UofC) and Sidney Nagel (UofC)

## Slide 2: Auxetic: Status and future plans
The current workflow has been tested on Midway up to 360 cores
The basic framework will remain:
Exploring search strategies:
  Control cases for comparison:
    Brute force
    Evolutionary algorithms (Good Swift use case)
  Current search evaluates all possible single cuts from a starting point, picks the best, and iterates from there
  Evaluating more than one cut at a time will provide more concurrency
Port to larger machine such as UofC Cray Beagle (should be straightforward)
Midway
Swift
Py
C++
Py
C++
Current state
All bonds
Select best cut